Validation Report
Name:
Validated IP: FIR Filter

TC#	Name
1	Global enable/disable
2	POR register values
3	Input buffer overflow and clearing
4	Filter bypassing
5	Signal processing

# Instance 1 (impl0)

TC#	Description	Pass/Fail
1	CSR access blocked when disabled and restored when enabled.	PASS
2	POR register values after reset do not match por.csv; mismatched fields: csr.sts, csr.rnd, coef.c1, coef.c2, outcap.hcap, outcap.lcap	FAIL
3	Input buffer counts 10 samples, overflows at 255, and clears correctly.	PASS
4	Bypass mode successfully relays input to output	PASS
5	Sample 0 mismatch: golden=0x18, impl0=0x38; likely wrong calculation or encoding.	FAIL

# Instance 2 (impl1)

TC#	Description	Pass/Fail
1	CSR access still allowed when disabled (global enable not enforced).	FAIL
2	POR register values after reset match por.csv	PASS
3	Input buffer counts 10 samples, overflows at 255, and clears correctly.	PASS
4	Bypass mode successfully relays input to output	PASS
5	Sample 0 mismatch: golden=0x18, impl1=0x0; output completely incorrect, possible initialization or input handling issue.

# Instance 3 (impl2)

TC#	Description	Pass/Fail
1	CSR access blocked when disabled and restored when enabled.	PASS
2	POR register values after reset do not match por.csv; mismatched fields: csr.sts, csr.ibcnt, csr.ibovf, coef.c1, coef.c2	FAIL
3	Input buffer count mismatch (expected 10, got 255) and clear failed.	FAIL
4	Bypass mode successfully relays input to output	PASS
5	All samples match golden model or fall within acceptable tolerance.	PASS

# Instance 4 (impl3)

TC#	Description	Pass/Fail
1	CSR access blocked when disabled and restored when enabled.	PASS
2	POR register values after reset do not match por.csv; mismatched fields: csr.sts, coef.c1, coef.c2	FAIL
3	Overflow flag not set when buffer reaches 255.	FAIL
4	Bypass mode successfully relays input to output	PASS
5	All samples match golden model or fall within acceptable tolerance.	PASS

# Instance 5 (impl4)

TC#	Description	Pass/Fail
1	CSR access blocked when disabled and restored when enabled.	PASS
2	POR register values after reset do not match por.csv; mismatched fields: csr.sts, coef.c1, coef.c2	FAIL
3	Input buffer counts 10 samples, overflows at 255, and clears correctly.	PASS
4	Bypass mode successfully relays input to output	PASS
5	All samples match golden model or fall within acceptable tolerance.	PASS

# Instance 6 (impl5)

TC#	Description	Pass/Fail
1	CSR access blocked when disabled and restored when enabled.	PASS
2	POR register values after reset do not match por.csv; mismatched fields: csr.sts, csr.rnd, coef.c1, coef.c2, outcap.hcap, outcap.lcap	FAIL
3	Overflow behavior incorrect (ibcnt=255, ibovf=0)	FAIL
4	Bypass mode successfully relays input to output	PASS
5	Sample 0 mismatch: golden=0x18, impl5=0x38; first output encoded incorrectly, verbose logging shows all outputs.	FAIL

TC1 Test Result

foreach ($i in "impl0","impl1","impl2","impl3","impl4","impl5") {
    Write-Host "==================== $i ===================="
    python final-project py -i $i -t tc1
    Write-Host ""
}

TC2 Test Result
foreach ($i in "impl0","impl1","impl2","impl3","impl4","impl5") {
>> Write-Host "==================== $i ===================="
>> python final-project.py -i $i -t por -f por.csv
>> Write-Host ""
>> }

TC3 Test Result

foreach ($i in "impl0","impl1","impl2","impl3","impl4","impl5") {
    Write-Host "==================== $i ===================="
    python final-project.py -i $i -t tc3
    Write-Host ""
}

TC4 Test Result
foreach ($i in "impl0","impl1","impl2","impl3","impl4","impl5") {
>> Write-Host "==================== $i ===================="
>>
>> # Run TC4 but only print the essential bypass info
>> python .\final-project.py -i $i -t tc4 | Select-String "Bypass OUT|Bypass Test"
>>
>> Write-Host ""
>> }

TC5 Test Result
(For p0.cfg only)
python3 final-project.py -i golden -t tc5 -f sqr.vec -c p0.cfg -p