Validation Report
Name:
Validated IP: FIR Filter

TC#	Name
1	Global enable/disable
2	POR register values
3	Input buffer overflow and clearing
4	Filter bypassing
5	Signal processing

# Instance 1 (impl0)

TC#	Description	Pass/Fail
1	CSR access blocked when disabled and restored when enabled.	PASS
2	POR register values after reset match por.csv	FAIL
3	Input buffer counts 10 samples, overflows at 255, and clears correctly.	PASS
4
5

# Instance 2 (impl1)

TC#	Description	Pass/Fail
1	CSR access still allowed when disabled (global enable not enforced).	FAIL
2	POR register values after reset match por.csv	PASS
3	Input buffer counts 10 samples, overflows at 255, and clears correctly.	PASS
4
5

# Instance 3 (impl2)

TC#	Description	Pass/Fail
1	CSR access blocked when disabled and restored when enabled.	PASS
2	POR register values after reset match por.csv	PASS
3	Input buffer count mismatch (expected 10, got 255) and clear failed.	FAIL
4
5

# Instance 4 (impl3)

TC#	Description	Pass/Fail
1	CSR access blocked when disabled and restored when enabled.	PASS
2	POR register values after reset match por.csv	PASS
3	Overflow flag not set when buffer reaches 255.	FAIL
4
5

# Instance 5 (impl4)

TC#	Description	Pass/Fail
1	CSR access blocked when disabled and restored when enabled.	PASS
2	POR register values after reset match por.csv	PASS
3	Input buffer counts 10 samples, overflows at 255, and clears correctly.	PASS
4
5

# Instance 6 (impl5)

TC#	Description	Pass/Fail
1	CSR access blocked when disabled and restored when enabled.	PASS
2		FAIL
3
4
5

TC1 Test Result

TC2 Test Result

TC3 Test Result